## Slide 1: Touchscreen
By Stacy Hicks

## Slide 2: Presentation Outline
Project Description & Goals
Hardware Used
Circuitry & Connections
Communication
Software & Programming
End Result

## Slide 3: Project Description, Motivation & Goals
Korry Electronics
  Electronics company which specializes in “human-machine interface”
    Area of focus: Cockpit controls
Motivation:
  The functionality and accuracy of touchscreen devices can degrade with repeated use.
  This is part of a larger project designed to test the breakdown of touchscreen accuracy over time
The goal of this project was to create a method for determining and recording the point at which the touchscreen “registers” the touch, so that this can be compared to the position of the actual touch

## Slide 4: Hardware
myRio
STMPE610 Controller
Touchscreen

## Slide 5: myRIO

## Slide 6: STMPE610 Controller
The STMPE610 controller receives the data from the touchscreen
The actual chip is in the center of the blue breakout board shown in photo to left

## Slide 7: Touchscreen
2 layer touchscreen with layers separated by dots
Effectively, the touchscreen is a voltage divider. When touched, circuit is completed and measured voltage tells position of registered touch

## Slide 8: Circuitry & Connections

## Slide 9: Synchronous Communication
STMPE610 controller uses either I2C or SPI communication which are both synchronous communication
  Unlike other methods, communication is an exchange of information
  During each communication event, the sender sends a bit and the receiver sends a bit back to the sender
Synchronous Communication use a “clock”
  For each falling edge of the clock a bit is transmitted (exchanged)
SPI (Serial Peripheral Interface) communication uses master/slave mode

## Slide 10: SPI Communication
SPI (Serial Peripheral Interface) communication uses master/slave mode
  MISO-Master In Slave Out
  MOSI-Master Out Slave In
MyRIO acts as Master
STMPE610 controller acts as slave

## Slide 11: Software & Programming Overview
Setup communication parameters
Startup & initialize commination with myRIO
Write/Read Data
Read Data
Output

## Slide 12: Main VI
True Case

## Slide 13: Main VI
False Case

## Slide 14: Main VI
User Interface

## Slide 15: Startup & Data Acquisition
“Startup” sub vi

## Slide 16: Write/Read Data

## Slide 17: Interpreting the Data

## Slide 18: Interpreting the Data
Lump coordinate information received in 4 bytes
X is 12 bits, Y is 12 bits, Z is 8 bits
Bytes come in as a hexidecimal address and x, y, z coordinate information must be separated from the 4 bytes written/read
X X
X Y
Y Y
Z Z

## Slide 19: Interpreting the Data
“Read” subvi

## Slide 20: Possible Future Work
Based on current results accuracy of touch readout could be improved.